## Slide 1: ECE-C432 Ch 4 Lecture 3
Ch 4 – Network Layer

## Slide 2: Broadcast Protocols
Protocols are needed so a node does not have to send multiple copies of the message to each recipient
Flooding – each node forwards message on every link except the one on which it came.
If there are cycles in the network graph, the no of messages circulating grows exponentially leading to ‘broadcast storm’.

## Slide 3: Broadcast Protocols (Contd)
Controlled flooding avoids broadcast storms. There are 2 methods:
Sequence number flooding – every node notes the source node and attaches a sequence no before forwarding the message. If the message arrives at the same node again due to cycling it can be identified and suppressed

## Slide 4: Broadcast Protocols (Contd)
Reverse Path Forwarding (RPF) .
In this method, a node will forward copies of the broadcast message only if it was received on the link which is on its shortest path to the source node
See example on p 402 and worked out example 4.4
Both these methods involve some amount of redundant messages though broadcast storm is avoided

## Slide 5: Broadcast Protocols (Contd)
Spanning Tree Broadcast – this method avoids all redundant messages and makes sure a copy of the broadcast message is received at every node
Involves constructing a spanning tree for the network and forwarding the broadcast message only along the edges of this tree
The spanning tree is constructed by first identifying a ‘center’ node. The other nodes then send ‘tree-join’ messages to this node. The message goes as far as some node which is already included in the spanning tree
See the example in the textbook and worked out example 4.5

## Slide 6: Multicast Groups
A multicast message is a message which is sent only to members of a group – e.g. messages sent to members of some user group, software updates sent to customers who have a licensed copy etc
A multicast group is assigned an IP-v4 address beginning 1110….. The address is for the whole group
Members of the multicast group have 2 IP addresses – their own unique unicast address and the multicast IP address of the group to which they belong

## Slide 7: Multicast Protocols
Internet Group Management Protocol (IGMP) is used between hosts and their directly attached routers
This enables a host to inform its router that it has joined (or left) any multicast group; it also enables the router to query its attached hosts whether any of them are members of a particular multicast group

## Slide 8: Group Shared Tree
Similar to forming a spanning tree for broadcasts (except that the tree may not include nodes which do not have hosts belonging to the multicast group)
The nodes which have at least one host belonging to the multicast group elect a center node among themselves
One of these nodes sends a “tree-join” message to the center which will be unicast along the least cost path to the center
Other nodes then send their “tree-join” messages which will propagate along the least cost paths to the center until they reach a node which is already part of the tree
If a node does not have hosts belonging to the multicast group, but is on the least cost path to the center from some other node , it must join the tree and multicast group messages
A node which does not have hosts belonging to the multicast group, and also not on the least cost path to the center from any other, node will not join the tree
See worked out example 4.6

## Slide 9: Source based Tree
Similar to Reverse Path Forwarding (RPF) for broadcast
The source node of the multicast will propagate the message along all outgoing links
If any other node receives the message along the link which is on the least cost path to the source, it will propagate the message along all outgoing links except the link on which it arrived; the node will block all other messages which did not arrive along the above-mentioned link
If a leaf node does not have any hosts belonging to the multicast group attached to it , it will send a “tree-prune” message to the upstream node. After this it will this node will not receive any group messages from the upstream router (this is where the protocol differs from the RPF broadcast protocol)
See worked out example 4.7

## Slide 10: Internet Multicast Protocols
The Internet multicasting protocols are:
- Distance Vector Multicast Routing Protocol (DVMRP). Implements source based routing with Reverse Path Forwarding (RPF)
- Protocol Independent Multicast (PIM)
Has 2 modes, ‘dense’ and ‘sparse’
Dense mode implements source based tree whereas sparse mode uses group-shared tree