## Slide 1: ECE-C432 Lecture 4.4
Ch 4 - Network Layer

## Slide 2: IP-v6 Addressing
IP-v6 has 128 bit source and destination addresses to enlarge the address space
The 128 bits must be separated into 8 fields of 16 bits each; each field must be written as 4 hex digits separated by colons thus: 3F45:8760:0AE5:76CC:FF98:0065:A098:0001
If there are a number of consecutive 0’s, they need not be explicitly written but denoted as ::, e.g. 3F45::0065:A098:0001 has 64 consecutive 0’s
However, it is illegal to write
3F45::0065::A098:0001 since it is not obvious how many 0’s are there in each ::

## Slide 3: Special IP-v6 Addresses
Some special addresses are as follows:
:: 128 0’s reserved for a newly booted host trying to get its IP address
:: 1 127 0’s followed by a 1 is loopback address used for testing
::192.168.2.2 - 96 zeros followed by IP-v4 address in dotted decimal notation is called IP-v4 compatible IP-v6 address used by a host which supports both IP-v4 and IP-v6 but connected to a router which supports IP-v4 only
::FFFF:192.168.2.3 - 80 zeros, followed by 16 ones then an IP-v4 address in dotted decimal notation is called IP-v4 mapped IP-v6 address used by a host which supports IP-v4 only but connected to a router which supports both IP-v4 and IP-v6
1111111……. IP-v6 address beginning with eight 1’s is a multicast address
An IP-v6 address which has 128 1’s is the broadcast address

## Slide 4: Normal IP-v6 addresses
Addresses used for unicasting are called Aggregatable Global Unicast Addresses
Currently they all begin with 001 and the remaining 125 bits are divided into 4 fields
Starting from the most significant they are:
TLA ID (13 bits) identifies continent
NLA ID (32 bits) identifies AS within continent
SLA ID (16 bits) identifies subnet within AS
Interface ID (64 bits) identifies the interface to which the address is assigned

## Slide 5: Site Local and Link Local Addresses
Any address beginning with 1111111011 followed by 38 0’s and then subnet ID and interface ID is called “Site Local” and the datagram will not be forwarded outside the ‘site’ (normally AS)
e.g. FEC0:: 1234:7A00:8657:DE34:0002
(1234 is SLA ID and 7A00:8657:DE34:0002 is Interface ID)
Any address beginning with 1111111010 followed by 54 0’s and then Interface ID is called “Link Local” and the datagram will not be forwarded outside the LAN
e.g. FE80:: 7A00:8657:DE34:0002 (last 16 hex digits are Interface ID)

## Slide 6: IP-v6 Datagram Format
Differs from IP-v4 format in the following respects:
Total length of the header is 40 bytes or 10 rows. Source and destination addresses occupy 8 rows
Length excludes header; max length of data is 65535 bytes; max length of datagram is 65575 bytes
Fragmentation not allowed except at source. So no fragmentation fields
Hop Limit corresponds to TTL in IP-v4
Next Hdr replaces Header length to indicate options
Flow Label is a new concept – all datagrams belonging to
the same ‘flow’ have the same label; e.g. while
downloading a video or audio file. Routers along the path treat these datagrams the same way
Checksum eliminated – error checking is done by TCP

## Slide 7: Interoperation of IP-v4 and IP-v6
In the present situation, Internet comprises both IP-v4 and IP-v6 nodes.
In the dual stack approach, IP-v6 capable nodes also run an IP-v4 stack and use this to replace the IP-v6 header by an IP-v4 header while communicating with IP-v4 only nodes. Note that Flow Label information is lost in this approach (Refer to Fig 4.25)
In the tunneling approach, IP-v6 nodes encapsulate an entire IP-v6 datagram within an IP-v4 datagram when communicating with IP-v4 only nodes . Flow Label information is preserved (Refer to Fig 4.26)